# Pos.	Quantity	Unit	Article/work			Unit price EUR	 	Total EUR

transfer:		_______,____

2.				Plastifloor-sealing

2.01			m²	Prime prepared surface until all

pores are sealed.

Material:		Plastifloor 112

Material consump:	0.5 kg/m² per layer until

all pores are sealed

Broadcast with quartz sand 0.2-0.7 mm.

_______,____		_______,____

OPTION

2.02			kg/h	Leveling works

Deep or large holes and cavities,

eruptions or extreme flaws in the

substrate are eliminated in advance

on site or on customer’s directive

by our staff on direct labour, with

wage and material cost statement.

technician work hour:

resin-based mortar: Plastifloor® 510

An even floor coating, corresponding

to  DIN 18202, can only be achieved if

a correspondingly even substrate

exists or is established on customer’s

directive.			_______,____		_______,____

2.03			m	Force-fitly cast elaborated construction

joints and cracks.

Joint dimension:

Material: 	Plastifloor 510

Consumption:	   kg/m		_______,____		_______,____

____________

Continued on page 3							transfer:	________,___

# Pos.	Quantity	Unit	Article/work			Unit price EUR	 	Total EUR

transfer:		_______,____

2.03a			m	Form elaborated expansion joints

in the structure permanently elastic.

or install a suitable metal joint profile.

Joint dimension:

Material.	Plastifloor 430

Consumption:	   kg/m		________,____	______,____

2.04			m²	Seal the coated surface.

Sealing must be effected until all

pores are sealed.

Material:		Plastifloor 526

Material consump:	0.5 -0.7 kg/m²

Colour: acc RAL colour chart_______,____	 	_______,____

3.				Site equipment

3.01			all in	- Setting up the site, provide tools

Machines during the whole con-

struction period.

- Executing and recording CM-measuring

- Executing and recording 1 bond strength

measurement

- Dispose of empty bundles environmentally

friendly

- Approach and departure from site 1 x

- Expense allowance for our staff

_______,____		_______,____

TITLE SUMMARY

1. Floor preparation

2. Plastifloor-sealing

3. Site equipment

____________

Net amount						_______,_____

VAT					____ %														_______,_____

------------------

Total amount																		_______,_____