Enquiry			Bill of Quantities for

Plastifloor( 418 s/l floor coating

for industrial floors (4 mm thickness)

| Pos. |  | Unit | Article / Description | Individual Price | Total Price |
| --- | --- | --- | --- | --- | --- |
|  |  |  | floor preparation |  |  |
| 1.01 |  | m² | mill surface with steel-ball blast plant 1-8 D, or with normal speed preparing edges with an angle grinder by hand | _______ , ___ | _____ , __ |
| 1.02 |  | m | open cracks closed with filler by using tools invoice concerning measurement | _______ , ___ | _____ , __ |
| 1.03 |  | m² | hoofing the surface with a vacuum cleaner | _______ , ___ | _____ , __ |
| 1.04 |  | m | open joints to shaft, to inlets, canal or machine using tools, the strengthened recessed joint realizes a better bond at the edge of the coat invoicing concerning measurement total: | ______ , ___ | _____ , __ _____ , __ |

| Pos. | Amount | Unit | Article / Description | Individual Price last page: | Total Price _____ , __ |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Plastifloor( - coating |  |  |
| 2.01 |  | m² | prime the prepared floor till closed pores material: Plastifloor( 112 material used: 0,5 kg/m² per level until the pores are closed broadcast with 0,6 – 1,2 mm quartz sand (slightly) contingency | _____ , __ | _____ , __ |
| 2.02 |  | kg / h | equalization deep or large holes, swells and cracks in the floor will be removed in advance, this happens by order of the owner concerning the record of wages and costs of material working hour: mortar based on resin: 510 an even (corresponding to DIN EN18202) coat can only be produced, if there is the necessary ground available or can be processed by order of the owner | _____ , __ | _____ , __ |
| 2.03 2.03a |  | m m | Processing joints seal rigidly size of the joints: material: Plastifloor( 510 + s/l filler (1:1) by volume consumption: kg/m form processed joints of movement permanent elastic within the construction or build in a joint profile material: Plastifloor( 430 consumption: kg/m | _____ , __ | _____ , __ |
| 2.04 |  | m2 | Spread out Plastifloor( 418 s/l coating with tooth rake, smooth with a smoothing trowel |  |  |
|  |  |  | total: |  | _____ , __ |

| Pos. | Amount | Unit | Article / Description thickness of the layer: 4 - 5 mm material used: 2,5 kg Plastifloor( 418 3,75 kg s/l filler color as required; RAL no. there are variations concerning color and mixture possible, but they do not result in claims of warranty producer: Plasti-Chemie Int. GmbH Zum Plom 35 D 08541 Neuensalz --------------------------------- phone: 0049 3741 55830 fax: 0049 3741 558327 | Individual Price last page: _____ , __ | Total Price _____ , __ _____ , __ |
| --- | --- | --- | --- | --- | --- |
| 2.05 |  | m² | sealing of the coated floor material: Plastifloor( 522 material used: 0,3 kg/m² | _____ , __ | _____ , __ |
| 3.01 |  | pau | site installations installation of the site, tools and machines stay at the site during the construction period CM-measuring and taking minutes 1 pull-off measuring and taking minutes disposal of empty boxes or pails transport to and from the site (once) allowance for the personnel | _____ , __ | _____ , __ |

|  |  |  | summary preparation of the floor Plastifloor( coating installation of the site net price VAT Total | last page: ______% | _____ , __ _____ , __ _____ , __ _________ _____ , __ |
| --- | --- | --- | --- | --- | --- |
| ° |  |  |  |  |  |